|  | ......................... Pcs. .............................. € .............................. € GEZE ActiveStop damping system integrated into the door leaf, for controlled dampened opening and closing of as well as keeping open swing doors on the interior. For doors with door leaf thickness from 38 mm Damping and closing from approx. 25° door opening angle, damping and opening from approx. 60° door opening angle. Free swing between 25° and 60°, opening and closing damping forces can also be adjusted via a valve in the installed state. Maximum door opening angle 140° Door opening angle can be set variably between 80° and 140°. Barrier-free in accordance with DIN 18040-2 due to low opening forces. The GEZE ActiveStop body is installed completely in the door leaf, the guide rail can only be seen when the door is open. Max. 45 kg door leaf weight, for left and right single-action doors |
| --- | --- |
|  | ......................... Pcs. .............................. € .............................. € Fixing plates for guide rails For securing guide rails in timber frames with insufficient screw-in depth of fixing screws |
|  | ......................... Pcs. .............................. € .............................. € Milling edge cover for the upper door rebate for covering the milling edge in case of rebated doors ( ) Milling edge coverage set GEZE ActiveStop white RAL 9016 ( ) Milling edge coverage set GEZE ActiveStop according to RAL ( ) Milling edge coverage set GEZE ActiveStop grey RAL 7035 |