|  | ......................... pc € .............................. € .............................. Panic lever lock set IQ lock EM DL for double-leaf doors Self-locking panic lever lock GEZE IQ lock EM DL for the moving leaf and with mechanical strike box for the fixed leaf as well as all required and tested components for double-leaf full panic doors in accordance with EN 179 and EN 1125! The moving leaf is also unlocked upon panic release of the fixed leaf. Panic unlocking via latch or panic bar Self-unlocking of both door leaves Changeover function for unlocking from outsid Divided and separated cross latch for absolute unencumbered crossbar projection without jamming even when preloaded; steel bolt 20 mm crossbar projection The electrically connectable exterior handle (fail secure version) facilitates unlocking from the outside. Daytime operation with permanently open position on the moving leaf can be achieved through permanent engaging of the exterior handle. Combines therefore well with access control systems. All required contacts are integrated in the lock and provide potential-free feedback: Deadbolt contact (with 95 % crossbar projection) Latch contact (with latch activation 10°) Cylinder contact Auxiliary lock contact (door open/door leaf enclosed) Release contact (exterior handle engaged) Prepared for installation of profile lock cylinders and with 9 mm square nut. Closed and corrosion-resistant steel lock case in DIN sizes, front metal and strike box in stainless steel Nominal voltage: 24 V DC Current consumption: 210 mA Supplied in a set comprising: 1 pc lever mortise lock IQ lock EM DL 1 pc mechanical strike box IQ lock DL with front metal 1 pc connecting cable 12-core 1 pc cable duct open 1 pc strike plate for receiving the lock upwards 1 pc switch lock 1 pc tubular pipe for locking upwards 1 pc solid rod for locking downwards 1 pc rod guide 1 pc floor lock hollow ( ) door leaf DIN right opening outwards / DIN left opening inwards ( ) door leaf DIN left opening outwards / DIN right opening inwards ( ) IQ lock EM DL 9235 (distance 92 mm, backset 35 mm) ( ) IQ lock EM DL 9240 (distance 92 mm, backset 40 mm) ( ) IQ lock EM DL 9245 (distance 92 mm, backset 45 mm) ( ) IQ lock EM DL 7255 (distance 72 mm, backset 55 mm) ( ) IQ lock EM DL 7265 (distance 72 mm, backset 6 5mm) ( ) IQ lock EM DL 7280 special backset 80 mm ( ) IQ lock EM DL 7210 special backset 100 mm For use in escape and rescue routes or in fire protection doors, fittings are required in accordance with EN 179 or EN 1125:. For approved fittings, please refer to the currently valid certificate versions 0757-CPR-229-7013137-5-2 / 0757-CPR-229PANIK-7013137-4 to certify the durability. Only GEZE components tested and approved together in accordance with EN 179 and EN 1125 may be installed! To ensure all functions of the IQ lock EL DL a door closer system with closing sequence control and a pushing flap are to be fitted. GEZE recommends ( ) 2 pc TS 5000 part no. 027333 ( ) 1 pc ISM guide rail part no. 115549 and ( ) 2 pc GEZE panic bars (EN 1125) configurable part no. 119005 |
| --- | --- |