|  | ......................... pc. € .............................. € .............................. Mechanical panic lock with contacts GEZE IQ lock C Self-locking mechanical panic lock with contacts GEZE IQ lock C for single-leaf doors tested and approved in accordance with EN 179 and EN 1125. Panic unlocking via latch or panic bar; changeover function for unlocking from the outside Divided and separated cross latch for absolute unencumbered crossbar projection without jamming even when preloaded! Prepared for installation of profile lock cylinders and with 9 mm square nut. Closed and corrosion-resistant steel lock case in DIN sizes, front metal of stainless steel; IQ lock C can be used for DIN left or right doors! Thanks to the integrated contacts the IQ lock C can easily be combined with emergency exit systems. All required contacts are integrated in the lock and provide potential-free feedback: Deadbolt contact (with 95 % bolt throw) Latch contact (with latch activation 10°) Cylinder contact Auxiliary lock contact (door open/door leaf enclosed) For use in escape and rescue routes or in fire protection doors, fittings are required in accordance with EN 179 or EN 1125:. For approved fittings, please refer to the currently valid certificate versions 0757-CPR-229-7013137-5-2 / 0757-CPR-229PANIK-7013137-4 to certify the durability Only GEZE components tested and approved together in accordance with EN 179 and EN 1125 may be installed! Please see the following EC certificates of conformity for approved fittings: 0757-BPR-229-09-003 / 0757-BPR-229-09-004 ( ) IQ lock C 9235 (distance 92 mm, backset 35 mm) ( ) IQ lock C 9240 (distance 92 mm, backset 40 mm) ( ) IQ lock C 9245 (distance 92 mm, backset 45 mm) ( ) IQ lock C 7255 (distance 72 mm, backset 55 mm) ( ) IQ lock C 7265 (distance 72 mm, backset 65 mm) ( ) IQ lock C 7280 special backset 80 mm ( ) IQ lock C 7210 special backset 100 mm Accessories: ( ) 1 pc. GEZE panic bars (EN 1125) configurable part no. 119005 ( ) 1 pc. connecting cable IQ lock part no. 103669 ( ) 1 pc. cable duct concealed part no. 106132 To ensure all functions of the IQ lock C a door closer is to be fixed to the door. ( ) 1 pc. TS 5000 part no.027333 |
| --- | --- |