|  | ......................... pcs. .............................. € .............................. € GEZE overhead door closer TS 5000 for all-glass doors, in accordance with EN 1154, with guide rail, with clamping plate for all-glass doors, closing force, closing speed, back check and latching action can be set from the front, with visual closing force display, installation on the hinge side ( ) TS 5000 closer body size EN 2-6, up to leaf width 1400 mm ( ) TS 5000 ECline closer body size EN 3-5, with very high efficiency > 80% for barrier-free doors in accordance with DIN 18040, up to leaf width 1250 mm ( ) TS 5000 SoftClose closer body size EN 2-6, up to leaf width 1,400 mm, for barrier-free doors in accordance with DIN 18040, up to leaf width 1,100 mm, quiet and safe closing even in changing pressure conditions, with one valve integrated in the closer body for the gradual adjustment of the end closing speed for braking or accelerating the door between 15° and 0° Alternative to the guide rail: ( ) with T-Stop guide rail, with integrated opening restrictor Colour: ( ) silver-coloured ( ) dark bronze ( ) white ( ) simulated stainless steel ( ) RAL .... |
| --- | --- |